## Slide 1: Introduction

## Slide 2: Capacitors and capacitance
  C = Q/Vab so Q = CVab
  Q increases as C is made larger, for a given pressure
    more capacity means more charge stored!
  Q increases as Vab increases
    For any particular capacitor, more pressure Vab allows it to hold more charge!
  But no voltage applied means no charge stored…

## Slide 3: Capacitors and capacitance
  The definition of capacitance is C = Q/Vab.
    Units of Capacitance: [Coulombs/Volt] = FARADs
    How much charge can you store per joule of work to keep them there?
    But [Volt] = [Joules/Coulomb]
    Farads = Coulombs2/Joule

## Slide 4: Evolution in Capacitors
Film dielectrics
“Wet” electrolytic capacitors
Ceramic Capacitors
Polymer Capacitors
Super Capacitors!
Graphene!

## Slide 5: Parallel-plate capacitor
  The capacitance of a parallel-plate capacitor is C = 0A/d

## Slide 6: Parallel-plate capacitor
  The capacitance of a parallel-plate capacitor is C = 0A/d.
  Note! C is engineered! You control Area & distance by design!
  C increases with Area
  C decreases with separation

## Slide 7: Parallel-plate capacitor
  The capacitance of a parallel-plate capacitor is C = 0A/d.
    So….0 = C x d/A = [Farads x meters/meters2]
    0 has units of [Farads/meter]
  Recall “0” from Coulomb’s Law: Force = (1/4p 0) q1q2/r2
    Units of 0 were Coulomb2/Newton-meter2
  So [Farads/meter] = [Coulomb2/Newton-meter2]
  [Farads] = [Coulomb2/Newton-meter]
  [Farads] = [Coulomb2/Joule]

## Slide 8: Parallel-plate capacitor
Example 24.2:
Plates 2.00 m2 in area; 5.00 mm apart; 10 kV applied Potential Difference.
    C= e0 A/d = 8.85 x 10-12 F/m *2.00 m2/.005 m = 3.54 x 10-9 F
    Q on each plate from C = Q/V so Q = CV = 3.54 x 10-5 C
    E field between plates from V = Ed so E = V/d = 2.00 x 10-6 V/m
    Or… E = s/e0 = (Q/Area)/e0 = 3.54 x 10-5 C/2.00 m2 / e0

## Slide 9: Capacitors in series
  Capacitors are in series if connected one after the other
  Equivalent capacitance of a series combination: 1/Ceq = 1/C1 + 1/C2 + 1/C3 + …
  NOTE
    Ceq is always LESS than the smallest capacitor in series!
      Say C1 = 10 mF, C2 = 20 mF, C3 = 30 mF
    1/Ceq = 1/10 + 1/20 + 1/30 = 6/60 + 3/60 + 2/60 = 11/60
    Ceq = 60/11 = 5.45 mF (< C1 !!)
  WHY?

## Slide 10: Capacitors in parallel
  Capacitors are connected in parallel between a and b if potential difference Vab is the same for all the capacitors.
  The equivalent capacitance of a parallel combination is the sum of the individual capacitances: Ceq = C1 + C2 + C3 + … .
  Note!
    Ceq is always MORE than largest capacitor in parallel!
      Say C1 = 10 mF, C2 = 20 mF, C3 = 30 mF
    Ceq = 10 + 20 + 30 = 60 mF > C3
  WHY??

## Slide 11: Calculations of capacitance
  Example 24.6, a capacitor network:
  Find C eq?

## Slide 12: Energy stored in a capacitor
  The potential energy stored in a capacitor is
        U = Q2/2C (in JOULES)
  U increases with more stored charge;
  U is less for fixed charge on a larger capacitor
  U = Q2/2C but C = Q/V…. so
        U = 1/2 QV.
  U = Q2/2C and Q = CV … so
        U = 1/2 CV2

## Slide 13: Energy stored in a capacitor
  The potential energy stored in a capacitor is
  U = Q2/2C = 1/2 CV2 = 1/2 QV.
  The capacitor energy is stored in the electric field between the plates. The energy density is u = 1/2 0E2.
  The Z machine shown below can produce up to 2.9  1014 W using capacitors in parallel!